## Slide 1: Architecture of microcontroller

## Slide 2: Embedded system
Purpose specific computer
  In contrast to a general purpose computer.
Used for automation
  Router that transmits packets automatically.
  A robot that can take judgment according to input form a sensor.
Microcontroller is used in embedded system
  Cheap
  Consume less power

## Slide 3: Microcontroller
On chip peripherals and memory
RISC
Harvard architecture
Advantages
  Cheap
  Less power
  Self sufficient

## Slide 4: Microprocessor
Perform raw calculation
CISC
Von Neumann architecture

## Slide 6: Atmel AVR Atmega8
Advanced RISC 8bit architecture
  Executes powerful instruction in one clock cycle.
  1 MIPS per Mhz.
  32 general purpose registers.
8Kb in system programmable flash
512 bytes of EEPROM
1KB of SRAM
23 general purpose I/O lines
Three flexible timers/counters
Internal and external interupts
SCI - USART
SPI
Two wire serial interface I2C
6 channel ADC with 10 bit accuracy
WatchDog timer
Power modes

## Slide 8: Registers

## Slide 11: Serial Communication
SPI
  Synchronous serial communication
  SCI
  Asynchronous serial communication
  RS232
  UART

## Slide 14: I2C – Inter integrated circuit
Proprietary of Philips
100Kbit/s 3.4 Mbit/s

## Slide 15: ADC
Digital signal processing.
Interfaces a MCU to physical world.

## Slide 16: PWM
Reverse process of ADC

## Slide 17: Thanks